## Slide 1: Implementing EU’s renewable target through green certificate markets.
by
Finn Roar Aune, Hanne Marit Dalen and Cathrine Hagem, Statistics Norway
Published in Energy Economics, 2012

## Slide 2: Bakgrunn
EU’s Climate and Energy Package:
  20 % reduksjon i klimagassutslipp
  Fornybar mål på 20 %.
Differensierte nasjonale fornybarmål (fra 10% to 49%).
Norge implementerte fornybardirektivet (67,5%).
Fornybardirektivet åpner for handel med fornybarkravproduksjon. (statistical transfers of energy from renewable sources)

## Slide 3: Bakgrunn/Problemstilling
Det handels med GHG-kvoter. Hvorfor ikke da også med fornybar energiproduksjon?
Utgangspunkt: Hvert land sitt fornybarkrav. Virkemidler: subsidiering av grønn energi, finansiert gjennom energiavgifter.
  Antar: Nasjonale grønne sertifikatmarkeder.
La p være markedsprisen på energi, β er prisen på sertifikater, og α er fornybarandel:
  Produsentprisen på grønn energi: p+ β.
  Konsumentprisen på energi: p+ α β.
To ineffektiviteter ved nasjonale sertifikatmarkeder:
    I produksjonen. Fornybar energi blir ikke produsert der det er billigst.
    I konsumet. «Energiavgiften» (α β) varierer mellom land
Hva er gevinsten av et felles EU-marked for grønne sertifikater handel, gitt differensierte fornybarkrav?
Hva er den ytterligere gevinsten av felles fornybarkrav (20%)
  Teoretisk og numerisk analyse for 2020 (Gml. Versjon av Libemod).

## Slide 4: Scenarier:
  Felles grønt sertifikat marked i EU, med felles fornybarandel.
  Felles grønt sertifikat marked i EU, med differensierte nasjonale fornybarandeler.
  Nasjonale grønne sertifikatmarkeder, med differensierte nasjonale mål.
I alle scenariene oppfylles målet om 20 % fornybarandel i EU (og 20% Klimagass reduksjon).

## Slide 5
Table 1: Effects of different implementations of the renewable directive in 2020 (annually)
compared with a CO2 target but no renewable target.
 | Domestic certificate trade only | EU-wide trade in certificates Number in brackets express the percentage changes relative to scenario iii) | 
 | Scenario iii) Differentiated national targets and no EU-wide trade in green certificates | Scenario ii) Differentiated national target and EU-wide trade in green certificates | Scenario i) Common renewable target and EU-wide trade in green certificates
Cost of introducing the renewable target (M €) | 19 522 | 5 968 (-69 %) | 5 745 (-71 %)
Change in producer surplus (M €) | 134 851 | 73 002 (-46 %) | 72 842 (-46 %)
Change in consumer surplus (M €) Change in taxes (M €) | -120 535 -33 838 | -49 401 (-59 %) -29 569 | -48 761 (-60 %) -29 831
Scenario iii): Certificate price = 47 €
Scenario i) and ii): Certificate price = 26 €
CO2 tax without/with the renewable target: 59€/52 €

## Slide 6
Figure 1: Countries’ yearly cost reduction in scenarios i) and ii) compared with scenario iii) as a share of their GDP.
Scenario iii) Differentiated targets-domestic certificate trade only
Scenario ii) Differentiated targets - EU-wide trade
Scenario i) Common targets – EU-wide trade

## Slide 7: Figure 2. Green certificate prices €/MWh
Scenario iii) Differentiated targets-domestic certificate trade only
Scenario ii) Differentiated targets - EU-wide trade
Scenario i) Common targets – EU-wide trade

## Slide 8: Konklusjoner
Differensierte nasjonale fornybarkrav gir ikke en kostnadseffektiv oppfyllelse av EUs samlete fornybarmål.
Kostnaden med å oppnå fornybarmålet kan reduseres med nesten 70 % gjennom handel med grønne sertifikater.
Et skift fra differensierte fornybarmål til et felles fornybarmål for alle land reduserer de samlete kostandene med ytterligere 4 %.
Handel med grønne sertifikater påvirker kostnadsfordelingen mellom land betydelig.

## Slide 9
Takk

## Slide 11
Table 1: Effects of different implementations of the renewable directive in 2020 (annually).
 | Domestic certificate trade only | EU-wide trade in certificates Number in brackets express the percentage changes relative to scenario iii) | 
 | System iii) Differentiated national targets and no EU-wide trade in green certificates | System ii) Differentiated national targets and EU-wide trade in green certificates | System i) Common renewable target and EU-wide trade in green certificates
Cost of introducing the renewable target (MEUR) | 19522 | 5968 (-69 %) | 5745 (-71 %)
Change in producer surplus (MEUR) | 173895 | 84938 (-51 %) | 84336 (-52 %)
Change in consumer surplus (MEUR) | -120535 | -49401 (-59 %) | -48761 (-60 %)
Change in taxes (MEUR) | -33838 | -29569 (-13 %) | -29831 (-12 %)
Change in carbon tax rate (EURO per tonne CO2) | -7.50 | -7.44 (-0.8 %) | -7.44 (-0.8 %)
Change in renewable energy consumption (Mtoe) | 30 | 34 (11 %) | 33 (11 %)
Change in gross final consumption of energy (Mtoe) | -60 | -29 (-51 %) | -30 (-50 %)
Change in electricity production (TWh) | -90 | -34 (-62%) | -26 (-71%)
Change in end-user electricity prices (EURO/MWh) | 7.39 | 3.35 (-55%) | 2.81 (-62%)
Change in producer prices of electricity (EURO/MWh) | -2.49 | -2.74 (10%) | -2.73 (9%)

## Slide 12
Green certificate price : iii) €47, ii) and i) € 26.