## Slide 1: MultiMOD – An equilibrium model for energy market & infrastructure analysis
Ruud Egging
24th Oct 2013
CREE meets CenSES
Notes: Credit: http://www.wpclipart.com/terms.html

## Slide 2: Research Objectives
Analyze trends in, and policy impact on energy markets, infrastructure developments and GHG emissions
What-if analysis
  scenario/policy assumptions
  impact on production, consumption, trade, infrastructure, fuel mix in power generation, GHG emissions, ….

## Slide 3: Research ambition
Integrated model, capturing all relevant energy market interactions in single model
  fuel substitution
  infrastructure developments
  market power aspects
  renewables integration
  climate policy
  Load & Seasonal variations
  Carbon leakage through goods trade
  Uncertainty

## Slide 4: Model actors overview
Suppliers
  “produce” and sell fuels and other energy carriers
  may be Cournot players vis-à-vis final demand
Arc operators
  allocate possibly congested transmission capacity, e.g., pipelines, LNG shipping, power lines, …
Transformation technology operators
  allocate transformation capacity of fuels, e.g, oil refineries, power plants
  technologies can include restrictions of certain input fuels relative to total output, e.g. mandate to add bio-fuel at a refinery

## Slide 5: Model actors overview continued
Storage operators
  allow suppliers to shift fuels over seasons/hours
Emission permit auctioneer
  allocates permits for various pollutants and green-house gases
  global, regional or nodal level
  emission trading and emission taxes
Final demand for energy
  linear inverse demand curve by sector.
  Linear substitution between different fuels
  fuel-specific (non-constant) efficiencies and end use costs.
  Restrictions on fuel mix and generation mix by sector and fuel can be included to represent regulation or technical constraints.

## Slide 6: Trade & supply relations illustration
Country B
Industry
Residential/Commercial
Country A
Uranium
Solar/Wind
Biomass
Coal
Oil
Gas
Gas
Transportation
Biomass
Industry
Residential/Commercial
Transportation
Power Generation
Refining/ Transformation
Power Generation
Refining/ Transformation

## Slide 7: Key actor: supplier
Supplier decides
  production
  trade (how much transport cap to use)
  transformation (refining & power generation(!))
  how much of what fuel/energy carrier to sell to demand sectors in each node
  …

## Slide 8: Supplier objective

## Slide 9: Supplier constraints

## Slide 10: Transmission System ('Arc') Operator

## Slide 11: Transformation technology operator

## Slide 12: Storage operator

## Slide 13: Emission Permit Auctioneer

## Slide 14: Final demand

## Slide 15
KKT's plus market clearing conditions MCP

## Slide 16: illustrations

## Slide 17: Data inputs
Production, consumption, transport, storage
Costs, capacities, efficiencies, loss rates, prices
No own forecasting, but calibrate models to reflect production & consumption in base year and forecasts from IEA, EIA, …
We add: country/infrastructure detail, market power assumptions, …

## Slide 18: Cases 'Focus on Germany'
Germany has announced an EnergieWende
Phasing out nuclear power
Full speed ahead with renewable energy
Recently, a major gas pipeline from Russia has been constructed.
Can Norway be a "Green Battery"?
What is impact on German energy market?

## Slide 19: German Energy context
Main European energy suppliers

## Slide 20: Germany
Nuclear phase out
Renewables plus 50%
Nord Stream I
Green battery Norway?
X

## Slide 21: German Supply Mix Power Generation (Mtoe after conversion)
Chart: 
| REF | Nuc PhOut | Nord Strm | Rnw +50% | Grn Batt | DEU combi
SOL | 26.0589 | 27.0103 | 27.0103 | 22.5249 | 26.0589 | 27.0103
REN | 7.0642 | 7.0642 | 7.0642 | 10.5982 | 7.0642 | 10.5982
GAS | 8.2647 | 8.2647 | 8.4326 | 8.2647 | 8.2647 | 12.3971
OIL | 0 | 0 | 0 | 0 | 0 | 0
HYD | 1.6302 | 1.6302 | 1.6302 | 1.6302 | 1.6302 | 1.6302
NUC | 12.0802 | 0 | 12.0802 | 12.0802 | 12.0802 | 0
export | -0.8369 | -1.7134 | -0.8316 | -0.643
import | 5.988 | 0.4135
Notes: *This Figure shows
*Phase Out: base load, imports
*Nord Stream: gas peak load, allows more base load, higher exports
*No-hydro Renew + 50%: push out coal (base load)
*NOR green batt: GER exports less
*Combi:

## Slide 22: Role of Norway..
Germany actually exports in reference case
In case studies Norway export only moderate amounts to Germany
But, what is missing in this model which might trigger much more trade between the two countries?

## Slide 23: CO2 tax EU-ETS

## Slide 24: Regional CO2 tax: Carbon Leakage?
What if Europe imposes a tax on CO2 emissions, and other regions don't?
Reduction in Europe partly undone due imports: carbon leakage
Should consider energy use for goods production..
Effects in energy-only model?

## Slide 25: CO2 emissions ref 2010 (tax $20/ton)
3.8 Gt
Giga ton = 103 bln kg
3.8 + 26.8 = 30.6 Gt
Notes: EU-ETS (REF = 3,800 Mton)
WORLD (REF = 30,600 Mton)
1274 is 33 % of EU-ETS reference emissions
1274 is 4.2 % of global reference emissions
825 is 2.7 % of global reference emissions

## Slide 26: ETS CO2 tax $60/ton
-548 Mt ( -14%)
Carbon leakage: 47%
- 548 + 256 = -292
Notes: EU-ETS (REF = 3,800 Mton)
WORLD (REF = 30,600 Mton)
1274 is 33 % of EU-ETS reference emissions
1274 is 4.2 % of global reference emissions
825 is 2.7 % of global reference emissions

## Slide 27: ETS CO2 tax $100/ton
-1274 Mt ( -34%)
Carbon Leakage: 35%
- 1274 + 449 = -825
Notes: EU-ETS (REF = 3,800 Mton)
WORLD (REF = 30,600 Mton)
1274 is 33 % of EU-ETS reference emissions
1274 is 4.2 % of global reference emissions
825 is 2.7 % of global reference emissions

## Slide 28: CO2-emission reductions and leakage for various EU-ETS tax levels
Chart: (Mton CO2)
| 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
EU-ETS (REF = 3,800) | -39.552 | 0 | 49.8548 | 107.5469 | 189.7101 | 291.6823 | 404.5364 | 515.5899 | 657.1939 | 825.0039
WORLD (REF = 30,600) | 57.0207 | 0 | -68.9461 | -135.9251 | -198.5554 | -255.5158 | -302.051 | -345.2013 | -382.8005 | -448.7489
Notes: *This graph shows
*The upper bars effective reduction
*Lower bars: part of ETS reduction compensated by additional in RoW
*Low tax: more than half
*Higher tax:
*Note $100  1/3 reduction ETS
EU-ETS (REF = 3,800 Mton)
WORLD (REF = 30,600 Mton)
1274 is 33 % of EU-ETS reference emissions
1274 is 4.2 % of global reference emissions
825 is 2.7 % of global reference emissions

## Slide 29: ongoing research

## Slide 30: Work in progress
Multi-period: endogenous capacity expansions
seasonality: demand variation and storage
supply load curves: renewables intermittency
Representing energy-intensive goods (CO2 leakage)
Master students:
  DIW: two finished: projections 2020
  Policy instruments in the European market
  Investment risk related to shale gas in Europe
  Decomposition
PhD Sophie: Uncertainty & multi-horizon scenario trees

## Slide 31: GEMSTONE/MultiMod
Insight in energy markets
Notes: Credit: http://commons.wikimedia.org/wiki/Category:Maps_of_the_world
Global Energy Market Model for Sustainability, Technology Options and Network Expansion.
"Equilibrium models for energy market and infrastructure analysis"
In this presentation I will discuss some of the problems and research objectives related to energy markets and infrastructure developments. I will clarify the limitations of optimization models for this type of research, and illustrate the use of equilibrium models (cast as mixed complementarity problems) and some insights that we can obtain when using such models.

## Slide 32: Credits
Green-blue globe:
  http://www.wpclipart.com/terms.html
World map:
  http://commons.wikimedia.org/wiki/Category:Maps_of_the_world